## Slide 1: Welcome to:
Maker Training Session
5:30 PM Tuesday, February 6, 2018
Broun Hall, Room 235

## Slide 2: Agenda

## Slide 3: About SPARC

## Slide 4: Introduction
Student lead organization at Auburn University.
Creates and fosters an environment of creativity and innovation through collaborative projects.
A place to test out ideas, integrate concepts learned in class, and learn skills that will be instrumental when working in the workforce.
No prior experience is required, only a willingness to learn.
Great for students of all ages and majors.

## Slide 5: Our Lab
Broun Hall
Room 367

## Slide 6: How to become a Member
Log 5 constructive hours in the lab
  Write the times on the sheet on the clipboard next to the door.
Contact us at sparc.auburn@gmail.com
We will respond with the instructions to get an access code.

## Slide 7: SPARC Meetings
Open Forum
  Discuss status of active projects
  Learn about and discuss specific topic in the realms of technology, engineering or making.
  Wednesdays at 6:00 PM
Maker Training Session
  Learn about a specific skills like 3D printing, CAD, electrical prototyping, and robotics.
  Centered around SPARC Sumo Bot Competition
  Tuesdays at 5:30 PM
Project Meetings
  Project members come together to talk about detailed progress.
  Meeting times and locations vary from project to project.

## Slide 8: Partner Organizations
NASA Robotics Mining Competition Team
  President: Jeremy Frasher <jjf0010@auburn.edu>
  Meets on Mondays 6-7, SPARC Lab, Broun 367
RC Hobbyist Club
  President: Craig Legrand <cbl0019@auburn.edu>
  Meets on Mondays 3:30-4:30, SPARC Lab
  Fridays 3:30-5:00, Broun 235
IEEE Auburn University Student Branch
  President: Michelle Kniffen <mek0027@auburn.edu>
  Meets on announced Mondays, Broun 238

## Slide 9: More Information about SPARC
Website
http://sparc-auburn.github.io/
Github
https://github.com/SPARC-Auburn
Slack
https://sparc-auburn.slack.com/
Email
sparc.auburn@gmail.com

## Slide 10: Meetings this Week

## Slide 11: Outreach

## Slide 12: Outreach Events
VEX Robotics Competition
  February 10, 2018 9am- 3pm
  Free Food and T-Shirt
Opelika HS FRC Team
  Help mentor a FIRST Robotics Competition (FRC) Team
  Mon Tue Thu: 3:30-6:30, Fri: 3:30-9:30, Sat:10-6
E-Day
  Help display projects in Broun, Student Center, and Concourse to high school students.
  Friday, February 23rd
Robot in 3 Days 2018 Bot
Engineering Tailgate 2016 SPARC Table
Notes: Fall 2016
  Loachapoka Robotics Mentoring- Mondays, Tuesdays, and Thursdays 3:00PM to 4:30PM
  ECE Minority Presentation- November 14th
  AJHS E-Day- November 17th
  South’s Best- December 3-4th
  SCORE Claw Machine- December 3-4th
Spring 2016
  E-Day- Late February or early March
  SPACE Day- Possible Event Next Semester
  IEEE Sumo Robotics Competition (with local middle and high schools)- Spring 2017

## Slide 13: Projects

## Slide 14: Spring 2018 Main Projects
MATILDA Robotics Platform
Tesla Coil
Unmanned Aerial Systems
Sumo Bot Competition

## Slide 15: Sumo Robotics Tournament

## Slide 16: What is a Sumo Bot Competition?
Two robots are placed in a ring
  Goal: attempt to push each other outside of ring.
  Typically autonomous
  First robot that touches outside of the ring loses the round.
The competitions “are non-destructive, family friendly, and great learning experiences.”
Classes of Sumo Bots
  Japanese class (< 6.6 pounds)
  Mini-class (< 1.1 pounds)
More information: http://www.robotroom.com/SumoRules.html
https://mcuoneclipse.com/2014/12/21/sumo-with-gopro-and-other-sumo-videos/
Mini Class
Japanese Class

## Slide 17: SPARC Sumo-Bot Requirements
Weight Constraint: < 750g(1.65lbs)
Size Constraints (at start of round)
  Width: 15cm (5.91”)
  Length: 15cm (5.91”)
  Height:
Robots must not
  Emit smoke or fire
  Leak, stain, or soil
  Disperse powder, grit, or grime
  Spray, throw, or use projectiles
  Jam, shock, or electromagnetically interfere
  Snare, entangle, or employ nets/rope
  Scratch, gouge, or scrape
  Have sticky/magnetic/suction wheels
XKCD: https://xkcd.com/1613/

## Slide 18: SPARC Competition Part Constraints
  up to 3 micro continuous servos
  up to 2 servo wheels
  all mechanical frame must be 3D printed
    no sheet metal or raw plastics allowed
  use any screws, nuts, washers
  use Arduino Nano (clones), protoboard, wires, etc.
  up to 2 Ultrasonic sensors
  up to 4 line following sensors

## Slide 19: Maker Training Sessions

## Slide 20: Maker Training Session Topics
Version Control (Git and GitHub)
3D CAD Parts (Solidworks)
3D Printing (Lulzbot Taz 3 w/ Cura Lulzbot Edition)
3D CAD Review and Assemblies (Solidworks)
Electrical Prototyping and intro to Arduino
Soldering and Electrical Fabrication
Basic Robotics Programming and PWM
Basic Sensor Programming

## Slide 21: Maker Topic: FDM and SLA 3D Printing

## Slide 22: Types of 3D Printers
Filament Based
  Fused Deposition Modeling (FDM)- like a glue gun
Resin Based
  Stereolithography (SLA)- UV single point laser cured liquid resin
  Digital Light Processing (DLP)- light projector cured liquid resin
Powder Based
  Selective Laser Sintering (SLS)- laser sintered powder
  Selective Laser Melting (SLM)- laser melted powder
  Electron Beam Melting (EBM)- electron beam melted powder
  Binder Jetting (BJ)- drop-on-powder and binding agent
  https://all3dp.com/1/types-of-3d-printers-3d-printing-technology/

## Slide 23: FDM vs. SLA 3D Printing
Category | FDM (Lulzbot Taz, etc.) | SLA (Form 2, etc.)
Printer Speed | Faster than average | Slower than average
Minimum Layer Thickness | 50 microns | 25 microns
Typical Printer Price | $200-$3000 | $2000-$20,000+
Material Cost (Per Kg) | $20-$40 | $150-$200
Post Processing | Remove supports | Remove supports/clean in I.P.A.

## Slide 24: How does FDM 3D Printing Work?
Use a process to form objects in successive layers vertically.
Use a “hot end” that works similar to a glue gun by melting a plastic filament to print each layer.
Many have heated beds to allow better heat distribution preventing the warping of printed objects.
Many use a honeycomb like internal structure to save material and time.
Examples of most popular 3D printing filaments:
  ABS
  PLA/PLA+
  HIPS
  Nylon

## Slide 25: Comparing Popular Filaments
https://www.3dhubs.com/knowledge-base/fdm-3d-printing-materials-compared

## Slide 26: Lulzbot Taz
Heated Bed
Filament
Hot End
Control Interface
Control Box / Power Supply
Tool Head

## Slide 27: Our Lulzbot
Lulzbot Taz 3
Hot end replaced w/ Hexogonal
Upgraded firmware
Side mounted heatsink fan
Side mounted bed fan
Heated bed w/ PET film
  soon to be upgraded to PEI

## Slide 28: Using Cura Lulzbot Edition
Design 3D model using CAD like SolidWorks, SketchUp, Autodesk, etc.
Save model as .STL file
Open in Cura Lulzbot Edition
Set printer settings such as temperatures and fill density
Generates Gcode File that printer can interpret
Press print or save to SD card

## Slide 29: How dOes SLA 3D Printing Work
UV light cures a liquid resin in a tank and cures onto a heated build platform.
Parts are built layer by layer but usually in an inverted orientation.
Isopropyl Alcohol bath is required to wash extra resin off of parts.
Flesh wire clippers are used to remove support structures.
Form 2 Marketing Video: https://www.youtube.com/watch?v=8tn5zA5bNSE&ab_channel=Formlabs
https://techcrunch.com/formlabs-form-2-laser-curing-open/

## Slide 30: Formlabs Form 2
Build Platform
Resin Tank
Control Screen
UV Shield
Resin Cartridge
Isopropyl Alcohol Wash Station
Post Processing Tools

## Slide 31: Types of Form Lab Engineering Resins

## Slide 32: Comparing Form Lab Resins
https://formlabs.com/materials/engineering/#rigid-overview

## Slide 33: Using Form Labs Pre Form
Design 3D model using CAD like SolidWorks, SketchUp, Autodesk, etc.
Save model as .STL file
Open in Form Labs Preform
Select Resin type and layer height.
Orient model and generate supports.
  Use isometric orientation where possible.
Press print to send instructions over to printer via WIFI, ethernet, or USB.

## Slide 34: Getting Models for 3D printing
Design your own
  SolidWorks, Autodesk Inventor, Fusion 360, Sketch Up, PTC Creo, etc.
Find .STL files online
  Thingiverse (https://www.thingiverse.com/)
  GrabCad (https://grabcad.com/)
  Yeggi (https://www.yeggi.com/)